## Slide 1: Classification of Signals with Common Variable Dependent Tones Occurring at Random Harmonics Using Machine Learning
Christopher Bell

## Slide 2: Outline
Motivation
Signal Model
Overview of Convolutional Neural Network (CNN) Architectures
Results

## Slide 3: Motivation

## Slide 4: Motivation
The goal of this project is to develop a machine learning (ML) algorithm to classify signals with common variable dependent tones
  Secondary goal is to determine if time domain or frequency domain-based convolution neural networks (CNNs) are more efficient
The presence of large numbers of overlapping tones makes classification of source mechanisms difficult
  Typically requires an experienced analyst and can not always be performed simultaneously with data collection
Examples of datasets with common variable dependent tones and harmonics include:
  Strucutureborne vibration data from rotating machinery
  Airborne noise data from drones
  Underwater acoustic data from ships or mammals
The use of machine learning algorithms to classify frequency spectra has been a significant area of study
  Machinery health faults (Sourza et. al. 2021)
  Detection of drones (Taha & Shoufan 2019)
This specific project uses structureborne vibration data from rotating machinery
  All source mechanisms are functions of shaft rate

## Slide 5: Motivation
denotes ball passing frequency of outer ring
denotes ball spin frequency
denotes ball diameter
denotes the number of balls
denotes pitch diameter
denotes the contact angle
denotes frequency
denotes revolutions per minute
denotes revolutions per second
denotes number of poles
denotes fundamental train frequency
denotes ball passing frequency of inner ring

## Slide 6: Signal Model

## Slide 7: Signal Model
Utilizing synthetic data
  No need to perform data collection
Tones can be generated in the time domain as a sum of sine waves
For each source (7 sources + no source case)
  Determine number of harmonics present by random sampling distribution
    e.g. 4
  Determine order of harmonics present by sampling without replacement a distribution for the total number of harmonics present
    e.g. [1, 8, 4, 3]
  Signal to noise ratio (SNR) of each harmonic was then set by random sampling distribution with replacement for each harmonic present
    e.g. [-10, 0, 6, 2]
  All present tones (for a data sample) are then summed with white gaussian noise (WGN) to make the data sample

## Slide 8: Signal Model (Cont.)
  denotes training sample
  denotes number of harmonics
10,000 data samples are made for each source (8,000 for training and validation)
Time domain signal is saved out for direct use in 1D CNN
  Sample rate =
  Time record is 1 second

## Slide 9: Signal Model (Cont.)
Fast Fourier transform (FFT) of time domain data is then calculated
  No averaging is conducted for FFT
  Frequency resolution of 1 Hz
Frequency domain data is used as input to 2D CNN
Frequency domain data is complex
  Cannot be converted to a grayscale image for input into the CNN
Solution is to stack the real and imaginary components before conversion to gray scale images
CNN Input
Spectral lines
Spectral lines

## Slide 10: 1D Convolutional Neural Network Overview

## Slide 11: 1D Convolutional Neural Network Overview
Input: Raw time data [1 x samples]
Convolutional Layers:
  Filter size: [1 x 8]
  Number of filters: 8
    Doubles for each successive convolution operation
    Pyramidal structure of data size
Normalization Layer
Activation Layers: ReLu
Global Max Pooling Layer
Dropout: 0.5
Optimization Algorithm: Adam
Minibatch size: 48
Number of Epochs: 5
Number of cross validation folds: 5
Input
1DConv
Normalization
ReLu
MaxPooling
Dropout
Fully Connected
1st Group
2nd Group
3rd Group
4th Group

## Slide 12: 2D Convolutional Neural Network Overview

## Slide 13: 2D Convolutional Neural Network Overview
Input: Stacked frequency domain data [2 x spectral lines]
Convolutional Layers:
  Filter size: [8 x 8]
  Number of filters: 8
    Doubles for each successive convolution operation
    Pyramidal structure of data size
Batch Normalization Layers
Activation Layers: ReLu
Pooling Layers: Window [1 x 2], Stride [1 x 2]
Dropout: 0.5
Optimization Algorithm: Adam
Minibatch size: 48
Number of Epochs: 5
Number of cross validation folds: 5
Input
2DConv
Batch Normalization
ReLu
MaxPooling
Dropout
Fully Connected
1st Group
2nd Group
3rd Group

## Slide 14: Results

## Slide 15
1D CNN Results
2D CNN Results
Cross Validation (5 folds)
  Accuracy: 95.15%
  Standard deviation: 0.22%
Significant decrease in accuracy below 2 dB peak SNR
Cross Validation (5 folds)
  Accuracy: 97.51%
  Standard deviation: 0.24%
  Consistent accuracy across all peak SNR

## Slide 16
1D CNN Results
2D CNN Results
Both networks have acceptable results, however 2D CNN has lower error rates overall
2D CNN has significantly higher accuracy for classes 3 through 8
Class 1 having the lowest accuracy is expected as all other sources are functions of source 1
Error is only correlated with overlapped source and not near sources for 2D CNN results
Notes: (compare class 3 and 4) and 6

## Slide 17: Conclusions & Next Steps
Conclusions:
  Successfully developed two CNNs for classification of signals with common variable dependent tones occurring at random harmonics
  Determined that the 2D CNN performed best
    Theory: The 1D CNN did not learn a more optimal method compared to the FFT to classify tones
  The 2D CNN also performed significantly better at low SNR
  Accuracy is correlated with pure tonal overlap
Future work:
  Transfer learning to other datasets
    Confirm the assumptions that went into the synthetic data
      For example, probability of harmonics is not uniform and varies significantly by mechanism
      Is equal probability assumption valid for training?
  Use on imbalanced datasets
    Not all sources occur with equal probability

## Slide 18: Questions?